## Slide 1: Ohm’s Law
The mathematical relationship between voltage, current, and resistance

## Slide 2: Warm Up Problems

## Slide 3: Definitions
Conductor:
  an object or type of material that allows the flow of electrical current
Insulator:
  A material of low conductivity that the flow of electrical current is not measureable.
Electromotive Force:
  Electric pressure that makes a current flow in a circuit. Unit is voltage
Voltage Drop (Usage):
  Voltage used by a resistor.
Current:
  Flow of the electrical charge.
Resistance:
  An object stopping or consuming electricity

## Slide 4: What is Ohm’s Law?
Ohm’s Law explains the relationship between voltage (electromotive force), Current (amps) and resistance (R)
Used by electricians, automotive technicians, small engine technicians, etc.

## Slide 5: Voltage
The push or pressure behind current flow through a circuit and is measured in volts (V).

## Slide 6: Current
The quantity/volume of electrical flow, measured in amps.

## Slide 7: Resistance
Resistance to the flow of current and is measured in Ohms 𝞨.

## Slide 8: Formula
  E= Voltage
  I = Current in Amperes
  R = Resistance in Ohms

## Slide 9: Problem 1
Find the missing measurement.
25
12.5

## Slide 10: Problem 1 Solution
Determine the formula by covering the missing value.
Replace the variables (letters) with the given values and solve.
Ω

## Slide 11: Problem 2
Find the missing measurement.
18
.75

## Slide 12: Problem 2 Solution
Determine the formula by covering the missing value.
Replace the variables (letters) with the given values and solve.
E = 18 x .75
E = I x R
V

## Slide 13: Problem 3
Determine the current flow through a compressor clutch that is operating on 14 volts with a 2.5 Ω of resistance.

## Slide 14: Problem 3 Solution
Determine the formula by covering the missing value.
Replace the variables (letters) with the given values and solve.
Amps

## Slide 15: Series Circuits
A complete circuit with more than one load
All of the current has only one path to flow through all the loads
Circuit must be CONTINUOUS in order for the current to flow through the circuit (think of old style Christmas lights)

## Slide 16: Series Circuits
Current remains constant
Voltage drops as current flows through a resistor
  V1 = I1 x R1
The sum of the voltage drop equals the applied voltage
An open or break anywhere in the circuit stops all current from flowing

## Slide 17: Series Circuits
Series Circuit Video

## Slide 18: Total Resistance
RT = R1+ R2+ R3
4 Ω
8 Ω
1 Ω

## Slide 19: Total Resistance
Find the Total Resistance
5.25 Ω
6.5 Ω
9 Ω

## Slide 20: Determine the Current?
14v

## Slide 21: Determine the voltage drop at each resistor.
14v

## Slide 22: Determine the total voltage
.12A

## Slide 23: Determine the voltage drop at each resistor
.12A

## Slide 24: Questions?